Individual Embedded Assignment #1
Abdullah Mortada	202200659

# Design Architecture

Above are the internal connections between components. Most of these components come pre-soldered onto the Arduino dev board.

The USB connector is used to power the whole system, and to interface by using the data pins on the connector. These pins are connected to a CH340 serial chip, which is necessary to enable communication between our system and a computer or other device.
The CH340 encodes the data into serial format, which is the format used for flashing Arduino ROM, and is the format needed for UART protocol, our protocol of choice for this project. The CH340’s clock signal is set by the crystal oscillator (note some ch340 chips have a built-in crystal) , and it’s internal reset is controlled by the atmega328’s reset pin. The RX and TX pins on the CH340 are connected to the TX and RX pins on the atmega328 respectively to enable full-duplex data transmission.
For our application, the atmega328 needs to be connected to an LED, and to a push button. The button is connected to a digital pin with the internal pull-up resistor and grounded on the other terminal.
# Software Implementation

All code and documents used are available on the github repo: https://github.com/abdullahmortada/EmbeddedProject1-23

The program runs using two interrupts, one which triggers when the button’s pin value changes, and the other is assigned to the RX pin, meaning it triggers when new data is loaded into the UDR register and clears when the buffer is flushed.

Button Interrupt handler: Simply checks if the button is pressed ( which would be value 0 as we are using	a pull-up resister ), and sends the string “button pressed\n” over UART if it is pressed.

RX Interrupt handler: Receives the new data from UDR, then adds it to a character array, as long as the	data received is not a newline character or end character, in which case the data is not	added to the buffer but instead sets a flag for the main loop to handle.

Main loop: Waits for the “received” flag, then disables the flag and compares the data in the character	array to the strings “led on” and “led off” using the standard library function “strncmp”. If	the string is a match the appropriate action to turn the led on or off is taken.

uart.c: Simple helper functions to complete UART protocol related functions, like setting the baud rate in	UBRR register, enabling RX and TX modes and transmitting and receiving data.

dio.c: Helper functions to control I/O ports, for setup and runtime.

Drivers

uart.c

Hardware Layer

Atmega328p
Ch340
USB connector

Middleware

dio.c

Application Layer

main.c

# Test Cases

Test Case	Action	Test Data	Expected Result	Actual Result	Pass/Fail
LED normal usage	Type “led on” in serial monitor	“led on\n”	LED turns on	LED turns on	pass
	Type “led off” in serial monitor	“led off\n”	LED turns off	LED turns off	pass
	Do not type anything		nothing happens	nothing happens	pass
LED incorrect usage	Misspell commands	eg. “ledop\n” or “led offf\n”	nothing happens	nothing happens	pass
	Type “led on” while on or off while off		LED stays in current state	LED stays in current state	pass
	Type random characters of correct length	eg. “eef zq” or “beg hr”	Data ignored	Data ignored	pass
	Insert an end character CR or new line character		nothing happens	nothing happens	pass
Button normal usage	Press button		“button pressed\n” shows in serial monitor	“button pressed\n” shows in serial monitor	pass
	Do not press button		nothing happens	nothing happens	pass
Button incorrect usage	Press button repeatedly		text printed in serial monitor the same number of times as there were pressed	text printed in serial monitor the same number of times as there were pressed	pass
	Hold button down		text printed one time only	text printed one time only	pass
	Press button while inputting “led on” in serial monitor		text printed on serial monitor and LED turns on	text printed on serial monitor and LED turns on	pass

# Bill of Materials
Un-optimized Samples During Development:
Part Name	Description	Price / LE	Link
Arduino Dev Board	Arduino rev3 board with atmega328p mcu and ch340 serial chip	240	https://makerselectronics.com/product/arduino-uno-rev3-smd
LED	LED	1	https://makerselectronics.com/product/led-green-8mm
Breadboard	small size breadboard	23	https://makerselectronics.com/product/breadboard-400-points
Button	2-terminal push button	0.75	https://makerselectronics.com/product/mini-push-button-2-pin-6x6x7-3mm
	Total / Unit	264.75

Optimized BOM for production:
Part Name	Description	Price / LE	Link
ATMEGA328PB SMD	microcontroller chip to be soldered on PCB	55 (1.78 $)	https://www.tme.eu/eg/en/details/atmega328pb-au/8-bit-avr-family/microchip-technology/?brutto=1&currency=USD&gclid=EAIaIQobChMI847QsojngQMVqDkGAB17fQjXEAQYASABEgIbbvD_BwE
CH340	USB to UART converter IC	27	https://uge-one.com/ch340g-usb-to-uart-ttl-converter-ic-smd-sop-16.html?gclid=EAIaIQobChMI0NvC6ITngQMVvUNBAh03KwwgEAYYAiABEgKP2_D_BwE
Custom PCB board	20 custom 2x4 PCB boards for 176 LE	9	https://www.nti.sci.eg/pcblab/
SMD 5V LDO voltage regulator	100mA 5V solderable voltage regulator to power MCU	1	https://uge-one.com/voltage-regulator-78l05-5v-100ma-smd-sot89.html
SMD push button	solderable push button	2	https://uge-one.com/smd-micro-push-button-switch-2p-3x4x2mm.html
SMD led	solderable led	1	https://uge-one.com/led-smd-1206-green.html
USB connector	USB connector to be soldered	3	https://makerselectronics.com/product/usb-connector-on-pcb-a-type-male-smd
Capacitor	SMD 10uF capacitor	1 x 3	https://uge-one.com/smd-chip-ceramic-capacitor-size-0805-10uf.html
Crystal oscillator	Quartz oscillator 16 mhz	5	https://uge-one.com/hc49-smd-quartz-crystal-oscillator-16mhz.html
	Total / Unit	106